## Slide 1: Hardware Software Platforms Project Presentation
DE1-SoC : Servomotor control
Fattahi Idriss and Honorez Valentin:
Idriss.FATTAHI@student.umons.ac.be
Valentin.HONOREZ@student.umons.ac.be

## Slide 2: Introduction and Motivations
MAIN GOAL  Control a servomotor with the DE1-Soc board with known solutions.
Objectives of the project :
  Doing technical researches.
  Improve VHDL skills.
  Implement existing works.
  Develop a driver and its test bench.
  Develop an application and its test bench.

## Slide 3: Theoretical background : Servomotor
Motorized system to reach predetermined positions.
Composed of:
  A motor.
  Gears.
  Electronics components.
Controlled by a PWM signal.

## Slide 4: Theoretical background : PWM signal
Binary signal.
Mean signal is an analogue signal.
Fixed period.
Duty cycle.

## Slide 5: Software to install
https://fpgasoftware.intel.com/?edition=lite
Quartus II
  Intel account creation
  18.1 Lite edition
CycloneV qdz file
  Launch the Device installer from Quartus II
ModelSim

## Slide 6: Project Creation
Launch Quartus II.
"New Project Wizard...“.
On the new window displayed:
  Select the folder
  Write the title of the project.
  Click on “Next”.
  Click on “Empty project” and on “Next”.

## Slide 7: Project Creation
Click "Next" on the "Add files" window.
On the "Family, Device and Board Settings" window:
  Select the family of component.
  “Next”.
Here it is a Cyclone V5CGXFC7C6F23I7.

## Slide 8: Project Creation
On the "EDA Tool Settings“:
  "ModelSim-Altera“.
  "VHDL".
Create a new file:
  Select "New“.
  Select "File“.
  Select "VHDL File“.
   Add existing files = Method explained before.

## Slide 9: How to simulate
Main code  top-level entity
Test bench file  properties  "VHDL Test Bench File".
Click on Assignments  EDA Tool Settings  Simulation:
  Output directory = Modelsim directory.
  Create a new Test bench.
  Test bench name/File name = VHDL file.
  Click on add.

## Slide 10: How to simulate
Click on Processing and start the compilation.
Click on Tools, Run Simulation Tool, RTL simulation.

## Slide 11: VHDL CODE
Divided in two parts :
PWM signal generation
Interface

## Slide 12: PWM signal generation
Period : 20 ms
Minimum pulse width : 0.5 ms (0 degrees)
Maximum pulse width : 2.5 ms (360 degrees)

## Slide 13: PWM signal generation
Altera Board clock : 100 MHz
We need a 64 kHz clock -> frequency divider
Why 64 kHz?

## Slide 14: PWM signal generation
Range of operation : 2 ms
Number of positions token by the servomotor : 128
 128/2ms = 64 kHz

## Slide 15: PWM signal generation
How to control the servo with the PWM ?

## Slide 16: PWM signal generation
Clock : 64 kHz
Position : 7 bits (128 positions)
Definition of a 10 bits counter (count till 1279 in order to browse the signal period (1280 samples per period).)
Definition of the pwmi signal : unsigned( ‘0’ + pos ) + 32
Servo signal == ‘1’ when count<pwmi else ‘0’

## Slide 17: PWM signal generation
Pos ‘0000000’ (which correspond to 0 degrees)
Pulse width : 0.5 ms
Total period : 20 ms

## Slide 18: PWM signal generation
Pos ‘1111111’ which correspond to 1 turn (360 degrees)
- Pulse width : 2.5 ms

## Slide 19: PWM signal generation
Position ‘0101000’ which corresponds to 112.5 degrees
- Pulse width : 1.10 ms

## Slide 20: Interface
Altera Board DE1 - SOC

## Slide 21: Interface: Diagram block of the behaviour of our program.